## Slide 1: CE331A Coordinate Transformation
Ibaad Anwar
Ashish Katiyar

## Slide 2
A coordinate transformation changes point positions from one coordinate system to another
Transforming Coordinates
Points AT and BT are the points correctly located in the To system.
Points AF and BF are the same points but in a the From system.
Points CF and DF are also in the From system and we would like to know their coordinates in the To system.

## Slide 3
Transformation elements
Scaling
Scaling is used to increase or decrease distances between the points in order to make them fit in the new system.
Rotation
The From coordinates must be rotated to make its directions coincide with those of the To system
Translation
The final element consists of two translations: shift positions in the North-South and East-West directions

## Slide 4
Transformation equation
  NG, EG are Global system coordinates
  NL, EL are To system coordinates
  TE, & TN are the translations in East and North directions
  ρ is the rotation angle
  S is the scale

## Slide 5
Transformation equation can be written as :
Where,
Transformation Equation in matrix form can be written as :

## Slide 6
After getting X, one can estimate the other coordinate
Solution :
Number of unknown = 4,
Number of equation from one point = 2
At least two point is required to get the solution
For redundant scenario, use least squares solution